Build the application

1- In file cmake.sh, set gcc arm toolchain directory in the variable TOOLCHAIN_DIR.
2- Run ./cmake.sh
3- cd <git repo>/build
    make
    make flash-murata_modem jlink-open

Module supported AT commands

Serial setting 115200 8N1

Command	Result	Function
AT+NRB	IDLAB_MURATA_LORA_DASH7_MODULE_BOOT / OK	Reboot
AT+MODE?	+MODE:<mode> / OK / <mode>: / - LORA / - DASH7TX / - DASH7RX / - DASH7TXRX	Get current module technology mode: LoRa, Dash7 TX, Dash7 RX or Dash7 TX RX. / The default mode is Dash7 TX.
AT+MODE=<mode> / <mode>: / - LORA / - DASH7	OK	Set module technology mode to LoRa, Dash7 TX, Dash7 RX or Dash7 TX RX.
AT+LORAPORT?	+LORAPORT:3 / OK	Get LoRa port. The default one is 3.
AT+LORAPORT=5	OK	Set LoRa port to 5.
AT+DEVEUI?	+DEVEUI:3432333852377418 / OK	Get device EUI.
AT+APPEUI?	+APPEUI:800000000000000d / OK	Get LoRa application EUI. / Default value is 800000000000000d.
AT+APPEUI=800000000000000e	OK	Set LoRa application EUI to 800000000000000e.
AT+APPKEY?	+APPKEY:86ae7ef1c15ff3e5c39e75ba84376576 / OK	Get LoRa application key. / Default value is 86ae7ef1c15ff3e5c39e75ba84376576.
AT+APPKEY=86ae7ef1c15ff3e5c39e75ba84376577	OK	Set LoRa application key to 86ae7ef1c15ff3e5c39e75ba8437657
AT+LORAJOIN?	+LORAJOIN:<status> / OK / <status>: / - NOT_JOINED / - JOINING / - JOINED / - FAILURE / - UNKNOWN	Get LoRa joining status.
AT+LORAMAXLEN?	+LORAMAXLEN:128 / OK	Get LoRa max allowed payload size. The maximum value that can be returned is 128.
AT+DASH7FILEID?	+DASH7FILEID:64 / OK	Get Dash7 file Id. The default value is 64.
AT+DASH7FILEID=32	OK	Set Dash7 file Id.
AT+SEND=1234567890	OK	Send 5 bytes 0x12, 0x34, 0x56, 0x78, and 0x90 via LoRa or Dash7 depending on the active mode.

Remarks

1- For sending data to the network, now the modem always returns OK even when an error occurred during sending. Handling sending errors, checking data length and returning Errors message should be done.

2- The maximum data to be sent depends on:
     - For Dash7: MODULE_D7AP_FIFO_COMMAND_BUFFER_SIZE: By default it is 100
     - For LoRa: LORAWAN_APP_DATA_BUFF_SIZE: set to 128
     - For both: MAX_SERIAL_RX_BUFFER_LEN: set to 256 means max 128 bytes to be sent
=> Enhancing maximum data to be sent should be done.

3- Some extra AT commads can be done to configure for instance dash7 setting…

4- Now supporting Rx data via dash7 is done but not with optimal way: the module will do foreground scan continuously, meaning RX is enabled all times and this is not suitable for battery powered device.
=> To be solved